## Slide 1: EMG Based Motion Capture [Project] From Motion Capture to Musculoskeletal Simulation and (not quite) back
Felix Laufer

## Slide 2: Recap: Why EMG Based Activation Estimation?
muscular redundancy
s.t.
classical stress minimization approach
What about …
co-contraction
fine motor tasks with higher muscle tension
extreme (fast) movements
(temporal / pathological) muscle fatigue … ?
neurophysiological redundancy /
activation patterns
s.t.
EMG informed minimization approach
Seminar: Approach 1
Project: Is surface EMG data (sEMG) a valid estimator
for computed muscle activation in practice?
?

## Slide 3: Project Setting & Motivation – MPI Study
MPI study suggests that sEMG is a useful predictor for muscle activation Goal := Verify that, reproduce results!
sEMG (8 muscles)

## Slide 4: Project Plan – Overview
Inverse Kinematics
joint angles
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
Arm model (musculosceletal)
OpenSim
+
MPI data
pointing movements
(joint kinematics)
computed muscle activations
(classical minimization approach)
sEMG measurements
(8 muscles)
Q1?

## Slide 5: Project Plan – A Look at the Source Data
MPI data
pointing movements
(joint kinematics)
computed muscle activations
(classical minimization approach)
sEMG measurements
(8 muscles)

## Slide 6: Actual Project – "Flowchart"
MPI study used commercial
full-body model (SIMM)
Choose open source full-body model
Conflicts with latest OpenSim version
Downgrade to earlier version
Different inverse dynamics algorithms
There are only antiquated free
full-body models!
Choose a free partial arm model
Partial arm model has been updated!
Complex mapping between full-body model data vs. partial arm model requirements ... finally works!
Classical minimization algorithm doesn‘t converge!
New model release requires new data mapping
Classical minimization algorithm converges ... but ...
Intermediate inverse dynamics results (joint torques) are totally different from study results!
Trial and error phase, change any parameter randomly

## Slide 7: Problem: Inconsistent Dynamics
Inconsistent inverse dynamics solution:
proximal joint torques very different!
But: distal joint torques (e.g. elbow) quite similar!

## Slide 8: Main Problem = Different Models
Inverse Kinematics
joint angles
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
"The proximal joints are much more complicated including lots of phantom joints and coupling to enable motion of the shoulder girdle so it makes total sense to me that if there is a discrepancy it is there, and not at the elbow […]“ (K. Saul)
Discussion with ...
Myroslav Bachynskyi Kate Saul (partial OpenSim community
(MPI study) arm model dev.) (simtk.org)
"Note that forces such as contact, ligaments, bushings, and even muscles will be applied to the model [during inverse dynamics]" (OpenSim Doc.)
"The arm model has restraint torques to mimic ligaments, and the full-body model probably doesn't.“ (K. Saul)
"Inertial properties of the SIMM full-body model might be [systematically] different to the partial arm model." (M. Bachynskyi)
Subject specific scaling of inertial properties is not possible.
(No participant information (mass, scale factors) contained in MPI data)
?

## Slide 9: Workaround: Restrained Movements
Since elbow torques are consistent ...
Alternative plan: Consider only elbow movement, restrain all other joints!
(1 free and 6 fixed DOFs)
 Compare only those computed activations vs. sEMG measurements related to elbow joint actuation: biceps, triceps
Restrained kinematics  different dynamics (elbow torque cannot be considered in isolation)
different dynamics  different computed muscle activations (stress minimization approach)
But ...
How comparable (w.r.t. study) are results under these restraints / assumptions?
... and ...
elbow actuated by biceps, triceps, brachialis, pronator teres, anconeus, ...
biceps / triceps actuate elbow, wrist (supination) / shoulder (adduction)
muscular
redundancy!
restrained elbow
movement
full movement sEMG
measurements
Thus ...
similar computed muscle activations
valid for ...?
yields ...?
still comparable ...?

## Slide 10: (Spurious) Results
r = 0.92, p < 0.01 (N = 170)
MPI study: correlations boxplot
biceps correlation: computed vs. sEMG
Authenticity of correlations "generated" with ...
different model
(inertia, internal forces, muscle properties, ...)
restrained kinematics
But there are also "spurious" correlations contained in the actual study results!
Correlate totally unrelated muscles:
e.g. pronator teres vs. deltoid  r = 0.74
Inverse Kinematics
joint angles
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
!

## Slide 11: Project Difficulties and Sources of Error
model scaling
marker points
distribution of body mass
…
MTU modelling
tendon slack length,
optimal fiber length
and maximum isometric force
…
EMG extraction and processing
surface EMG only (no deeper MTUs)
characterizing frequency bandwidths
 generalizability?
generalizability (subject  model)
individual neural drive and activation strategies
MTU params highly dependent on subject
(neuro)muscular redundancy
muscular := several muscles for one joint or muscles spanning multiple joints
neurophysiological := task-dependent activation strategies or multiple neurons innverating the same muscle
co-contraction
EMG  muscle activation muscle forces
mapping poorly understood,
no reliable models
inverse dynamics
measure of external forces
distribution of body mass
numerical errors
inverse kinematics
drift of markers
joint modelling
numerical errors
marker placement & tracking
real vs. virtual markers
tracking accuracy
repeatability
Inverse Kinematics
joint angles
Motion Capture
marker trajectories
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
joint angles
Motion Simulation
marker trajectories
muscle activation and forces
forces, torques
Forward Kinematics
Forward Dynamics
Musculoskeletal Modelling

## Slide 12: Thanks for your attention! From Motion Capture to Musculoskeletal Simulation and (not quite) back
Questions?
Theory
Practice
vs.
Seminar
Project
vs.

## Slide 13: Assuming that sEMG is a valid estimator ...