## Slide 1: EMG Based Motion Capture [Seminar] From Motion Capture to Musculoskeletal Simulation and back
θ
θ
θ
Felix Laufer
M
M
M
F
F

## Slide 2: Why Musculoskeletal Simulation?
Sports
Analyze and improve athletic performance
HCI
Human Computer Interaction
Industrial Ergonomics
Design ergonomically safe environments
Biomechanical Basic Research
Understand the human
locomotion system in detail
Medicine
Investigate and treat movement disorders
Build wearable assistive devices (orthoses and prostheses)

## Slide 3: From MoCap to Musculoskeletal Simulation
Inverse Kinematics
joint angles
θ
θ
θ
skeletal model,
kinematic chain
Motion Capture
marker trajectories
marker
points
Musculoskeletal Simulation
muscle activation and forces
?
M
M
M
F
F
Inverse Dynamics
forces, torques
body model,
mass distribution,
inertia matrix, …
external
forces, GRF, …

## Slide 4: Musculoskeletal Modelling
Musculo Tendon Unit (MTU)
abstract model of motor neurons including all innervated muscle fibers and the tendon of a commonly controlled skeletal muscle based on hill‘s model
Hill‘s muscle model
Musculoskeletal Models

## Slide 5: Muscular Redundancy and the DOF Problem
shoulder pitch
shoulder roll
shoulder yaw
elbow pitch
wrist yaw
wrist pitch
elbow roll
Arm excluding hand:
7 kinematic DOF but > 20 skeletal muscles
complex mapping!
joints are over-actuated  muscle system is underconstrained
multiple solutions of the inverse muscle Jacobian
segment forces, torques
muscle activation and forces

## Slide 6: The (classical) Optimization Approach
Idea: Pick the solution that minimizes total muscle stress!
Treat the desired / measured dynamics as constraints
and the sum of generating muscle forces / activation of
muscles as a global performance criterion to be minimized
s.t.
Always an appropriate method for estimating muscle forces / activation?
What about …
co-contraction
fine motor tasks with higher muscle tension
extreme (fast) movements
(temporal / pathological) muscle fatigue … ?
neurophysiological redundancy
several MTU recruitment
strategies for different motor tasks

## Slide 7: EMG Data for Estimating Muscle Activation
Electromyography (EMG)
Electrodiagnostic technique for detecting accumulated action potentials
of a skeletal muscle (group) generated by the associated motor neurons
Signal Processing
Idea: Use EMG data for estimating the wanted muscle activation!
Treat the EMG data corresponding to the wanted muscle activation
as additional contraints
s.t.
solvability!

## Slide 8: The other Way round – EMG Forward Simulation
Idea: Use EMG data to directly drive a model‘s forward dynamics!
Inverse Kinematics
joint angles
Motion Capture
marker trajectories
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
Motion Simulation
Forward Kinematics
Forward Dynamics
Musculoskeletal Modelling
Common Approach: Single DOF Model
Model predicting the joint moment at one single calibrated DOF from EMG data recorded at the associated MTU
hip pitch (FE)
hip roll (AA)
knee pitch (FE)
rectus
femoris
MTU
rectus femoris EMG data
Single DOF models produce valid solutions for each DOF separately
but inconsistent solutions amongst multiple DOF
Again, the redundancy / DOF problem!
Single DOF models can address neurophysiological redundancy for a certain DOF but not muscular redundancy in terms of multiple DOF.

## Slide 9: EMG Forward Simulation – Multi DOF Model
Idea: Build a Multi DOF Model calibrated for several DOF  consistent force solution!
optimization

## Slide 10: Multi DOF Model – Results
hip pitch (FE)
hip roll (AA)
knee pitch (FE)
rectus
femoris
MTU
rectus femoris EMG data
Force (N)
Running task: rectus femoris

## Slide 11: General Difficulties and Sources of Error
model scaling
marker points
distribution of body mass
…
MTU modelling
tendon slack length,
optimal fiber length
and maximum isometric force
…
EMG extraction and processing
surface EMG only (no deeper MTUs)
characterizing frequency bandwidths
 generalizability?
generalizability (subject  model)
individual neural drive and activation strategies
MTU params highly dependent on subject
(neuro)muscular redundancy
muscular := several muscles for one joint or muscles spanning multiple joints
neurophysiological := task-dependent activation strategies or multiple neurons innverating the same muscle
co-contraction
EMG  muscle activation muscle forces
mapping poorly understood,
no reliable models
inverse dynamics
measure of external forces
distribution of body mass
numerical errors
inverse kinematics
drift of markers
joint modelling
numerical errors
marker placement & tracking
real vs. virtual markers
tracking accuracy
repeatability
Inverse Kinematics
joint angles
Motion Capture
marker trajectories
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
joint angles
Motion Simulation
marker trajectories
muscle activation and forces
forces, torques
Forward Kinematics
Forward Dynamics
Musculoskeletal Modelling

## Slide 12: Thanks for your attention! From Motion Capture to Musculoskeletal Simulation and back
Questions?

## Slide 13: Appendix – Hybrid Approach
Idea: Combine both forward and inverse simulation in order to obtain, validate and refine internal parameters and models at any point in time!
 successively estimate unknown model components and drive prediction errors to zero
Inverse Kinematics
joint angles
Motion Capture
marker trajectories
Musculoskeletal Simulation
muscle activation and forces
Inverse Dynamics
forces, torques
joint angles
Motion Simulation
marker trajectories
muscle activation and forces
forces, torques
Forward Kinematics
Forward Dynamics
Musculoskeletal Modelling
validate
validate
validate
validate